## Slide 1
What is the Standard Base we
work with in our everyday lives?
Number Systems
Why do we work in that base?
Lab 11

## Slide 2
Common Bases
2 – 1010 0100
8 - 5672
10 – 78645
16 – ABC983EF
Open
bases.java

## Slide 3
What is 235 really?
Is it 235 or is there more to it?
In actuality, 235 is
2 * 10 to the 2nd power (100) +
3 * 10 to the 1st power (10) +
5 * 10 to the 0th power (1).
If you add these up you end up with 235.
base 10

## Slide 4
You can convert any base to base 10 by following the power system.
All number systems regardless of the base work off of the same principles.
Any base to base 10

## Slide 5
Given 32 in base 4, you could convert it by
43 42 41 40
* * * *
0 + 0 + 3 + 2
0 * 64 + 0 * 16 + 3 * 4 + 2 * 1
32 in base 4 is 14 in base 10
Any base to base 10

## Slide 6
Given the base 10 number 70, you could convert
it to base 5 following these easy steps :
base to num10 remainder
1st divide 70 by 5 5 | 70 0
2nd divide 14 by 5 5 | 14 4
3rd divide 2 by 5 5 | 2 2
0
The number 70 base 10 = 240 in base 5.
Base 10 to any base

## Slide 7
1st - Convert the number you want
to convert to Base 10.
2nd - Convert the Base 10 result to the
new base you want.
Any base to any base

## Slide 8
binary - base 2
 | Binary digits |  |  | 
Base 10 | 8 | 4 | 2 | 1
1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0
3 | 0 | 0 | 1 | 1
4 | 0 | 1 | 0 | 0
5 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0
7 | 0 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0

## Slide 9
There is a direct conversion from base 2
to base 8 & base 16 without using base 10.
8 and 16 are powers of 2 so they convert
directly.
base 2 to base 16

## Slide 10
Base 2 converts directly to base 16 as each
4 bit section of base 2 equals one base 16
digit.
1111 = 15 15 is maximum single digit for 16
10 11
1010 1011 = AB in base 16
1 4 10
0001 0100 1010 = 14A in base 16
base 2 to base 16
HEX
A – 10
B – 11
C – 12
D – 13
E – 14
F – 15

## Slide 11
Base 2 converts directly to base 16 as each
3 bit section of base 2 equals one base 8
digit.
111 = 7 7 is maximum single digit for base 8
5 3
101 011 = 53 in base 8
1 2 7
001 010 111 = 127 in base 8
8
base 2 to base 8

## Slide 12
java base conversion
int base10 = Integer.parseInt("324",6);
out.print("324 base 6 == ");
out.println(base10 + " base10");
out.print("124 base10 == "); out.println(Integer.toString(base10,16)+" base16\n\n");
out.println(Integer.toBinaryString(90));
out.println(Integer.toOctalString(90));
out.println(Integer.toHexString(90).toUpperCase());
OUTPUT
324 base 6 == 124 base10
124 base10 == 7c base16
1011010
132
5A

## Slide 13
Open
javabase.java
java base conversion

## Slide 14
Adding and Subtracting
in any Base!!!!

## Slide 15
Adding and Subtracting
in any Base!!!!
145
+ 345 base 8
512 base 8
149
+ 345 base 12
492 base 12
427
345 base 9
72 base 9

## Slide 16
Binary Operators
AKA Bitwise Operators
& | ^ << >>
These operators manipulate the binary digits
of variables.

## Slide 17
Operator Precedence
() | HIGH
! ++ -- | 
* / % | 
+ - | 
<< >> (bitwise shifts) | 
< <= > >= | 
== != | 
& (bitwise and ) | 
^ (bitwise xor ) | 
¦ (bitwise or ) | 
&& | 
¦¦ | 
= += -= *= /= %= | 
, | LOW

## Slide 18
Bitwise AND &
int one=9;
int two=7;
out.println(“9 & 7 == " + (one&two));
OUTPUT
9 & 7 == 1
binary representation |  |  |  | 
 | 8 | 4 | 2 | 1
one | 1 | 0 | 0 | 1
two | 0 | 1 | 1 | 1
result | 0 | 0 | 0 | 1

## Slide 19
int one=9;
int two=7;
out.println(“9 | 7 == " + (one|two));
OUTPUT
9 | 7 == 15
Bitwise OR |
binary representation |  |  |  | 
 | 8 | 4 | 2 | 1
one | 1 | 0 | 0 | 1
two | 0 | 1 | 1 | 1
result | 1 | 1 | 1 | 1

## Slide 20
int one=9;
int two=7;
out.println(“9 ^ 7 == " + (one^two));
OUTPUT
9 ^ 7 == 14
Bitwise XOR ^
binary representation |  |  |  | 
 | 8 | 4 | 2 | 1
one | 1 | 0 | 0 | 1
two | 0 | 1 | 1 | 1
result | 1 | 1 | 1 | 0

## Slide 21
open
bitwiseand.java
bitwiseor.java
bitwisexor.java

## Slide 22
Bitwise Shift Left <<
int one=8;
out.println("8 << 1 == " + (one<<1));
OUTPUT
8 << 1 == 16
SHORTCUT
<< 1 multiplies by 2
16 | 8 | 4 | 2 | 1
0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0

## Slide 23
Bitwise Shift Right >>
int one=8;
out.println("8 >> 1 == " + (one>>1));
OUTPUT
8 >> 1 == 4
SHORTCUT
>> 1 divides by 2
16 | 8 | 4 | 2 | 1
0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0

## Slide 24
open
shiftleft.java
shiftright.java

## Slide 25
Start work
on Lab 11